## Slide 1
Advanced Image Processing and Machine-learning Techniques for Film Restoration
Student Name: TANG Zhiheng
Student ID: 17083046d
Programme Code: 42470
Supervisor(s): Dr Lam Kim-Man
Submission Date: Dec 21, 2020
The Hong Kong Polytechnique University
Department of Electronic and Information Engineering

## Slide 2
CONTENTS
Introduction
Literature Review
HMM Detection and Restoration
CNN Detection and Restoration
Deep Image Prior Denoising
01
02
03
04
05
Conclusion
06

## Slide 3
Introduction
PART 01

## Slide 4
01 Introduction
Archive films often suffer physical or chemical degradation through improper storage and repeatedly playing. The possible artifacts include white noise, dirt, sparkle, blotches, and scratches, appearing in different forms with random size and position.
This project will investigate and evaluate different techniques to build a generic detection and restoration framework with reasonable quality control.

## Slide 5
01 Introduction
Target:
Detect, remove and restore Dirt, blotches, and sparkle
Common ground:
Appear in a single frame
Create discontinuity and sudden intensity difference
Random size and position
Sometimes, the artifacts are mixed with noise, blur and unalignment. Usually, several methods are combined to complete one target.

## Slide 6
Literature Review
PART 02

## Slide 7
02 Literature Review
Filter-based method:
Storey [1]: Threshold on maximum variation for dirt removing
Kokaram [2]: SDIp: Use motion-compensated pixel values to reduce moving interference
[2] Kokaram, A. C., & Rayner, P. J. System for the removal of impulsive noise in image sequences. In Visual Communications and Image Processing'92 (Vol. 1818, pp. 322-331). International Society for Optics and Photonics, 1992.
[1] R. Storey,“Electronic detection andconcealment of film dirt,” J. Soc. Motion Picture Telev.
Eng., vol.94, no.6, pp.642–647, Jun.1985.
[3] X. Wang and M. Mirmehdi, "Archive Film Defect Detection and Removal: An Automatic Restoration Framework," in IEEE Transactions on Image Processing, vol. 21, no. 8, pp. 3757-3769, Aug. 2012.
Model-based method:
Wang and Mirmehdi [3]: Proposed artifact detection using Hidden Markov Model in effect of novelty detection.

## Slide 8
02 Literature Review
[5] A. Krizhevsky, I.Sutskever, and G.E.Hinton,“Imagenet classification with deep convolu-
tional neural networks,” Communications of the ACM, vol.60, no.6, pp.84–90, 2017.
[4] Y. LeCun, L. Bottou, Y. Bengio, and P. Haffner,“Gradient-based learning applied to docu-
ment recognition,” Proceedings of the IEEE, vol.86, no.11, pp.2278–2324,1998.
LeCun et al. [4]: LeNet
Krizhevsky, Sutskever and Hinton [5]: AlexNet: More layers
Yous, Serir, and Yous [6]: Segnet: Semantic segmentation
[6] H. Yous, A. Serir, and S. Yous,“Cnn-based method for blotches and scratches detection in archived videos,” Journal of Visual Communication and Image Representation, vol.59, pp. 486–500,2019, ISSN: 1047-3203

## Slide 9
HMM Detection and Restoration
PART 03

## Slide 10
03 HMM Detection and Restoration
Hidden Markov Model (HMM) is a statistical Markov model in which the system being modeled is assumed to be a Markov process
Hidden Markov Model (HMM)
Hidden State
Observation Sequence
(Pixel Value)
Emission Matrix
(To train)
Transition Matrix
(To train)
HMM Model
Through training, HMM can remember the characteristic of a certain pattern or sequence.
If the similarity between the upcoming sequence and the learned sequence is high, the model forward and backward probability will be high

## Slide 11
03 HMM Detection and Restoration
Novelty detection:
HMM model attempts to evaluate how "normal" a sequence of pixels is. To learn natural patterns, the HMM model is trained by pixel sequences from artifacts-free movie frames.
Any sequence that deviates from the natural sequence can be regarded as artifacts candidates.
Normal – High Value
Main idea of Hidden Markov Model Detection(HMM)
3 4 3 5 4 3 2 3 …
Abnormal – Low Value
3 4 3 5 10 3 2 3 …
Spike

## Slide 12
03 HMM Detection and Restoration
HMM Setup
HMM Model
The model is constructed as 7 observation states and 5 hidden states, as proposed by Wang and Mirmehdi [3]. The sequence length is set as 13
[3] X. Wang and M. Mirmehdi, "Archive Film Defect Detection and Removal: An Automatic Restoration Framework," in IEEE Transactions on Image Processing, vol. 21, no. 8, pp. 3757-3769, Aug. 2012.
By setting hidden states = 5, the model state transition can be interpreted as transition between background and foreground.
The reason why observation states is set 7 but not 255 is that too many observation states introduces too much variation and makes the learning very difficult. Setting small number of observation states is to reduce the computational burden and effect of noise.

## Slide 13
03 HMM Detection and Restoration
Dataset Link:
http://dspv.eie.polyu.edu.hk/video_meiah/
Two Image Sets
Original Image Set
Ground Truth (Artifacts-free)
Dataset Size:
2909 Frames (1300*2100)
Original Image Set
Ground Truth

## Slide 14
03 HMM Detection and Restoration
Training sequences extraction:
Use the current frame and previous 6 frames and following 6 frames to construct a 13 consecutive frames.
Convert the frames to gray scale.
Randomly choose 10000 pixels and sample their values in 13 frames. The sampling result forms an array of size (13, 10000).
Uniformly map the values of the (13, 10000) from 0-255 to 0-6.
Ground Truth
Update
Get Final Model Parameters
Model parameter updating:
Use the Baum-Welch method
to update the parameters of HMM model
Frame selection requirements:
The selected frames should be consecutive frames in a single scene.
There are both background (static) region and foreground (moving) region
The motion should be moderated

## Slide 15
03 HMM Detection and Restoration
Sequence Evaluation:
Main Idea: If a member is removed and the sequence becomes normal, the member should be an artifact.
1. Leave the k-th(0-13) component out and evaluate the remaining sequence’s degradation possibilities one by one.
2. Normalize the result of removing the center component with the sum of the 13 results.
Examine model response to “Spike”
Uniform state -> Low value
Spike -> High value
If the trained model does not show the above characteristic, retrain it until a good model is obtained.

## Slide 16
03 HMM Detection and Restoration
1. The HMM returns a u value to each pixel. Perform thresholding on u to obtain defect map
Too many false alarms
Threshold too low
HMM Initial Detection
Threshold = 0.5
Threshold = 0.1
Perfect detection
Threshold just right
Detection loss
Threshold too high
Threshold = 0.8

## Slide 17
03 HMM Detection and Restoration
False alarm caused by motion
Artifact is covered
2. Assume the artifacts do not appear at the same location on neighboring frames.
Eliminate the candidates appearing in both frames using 8-connectivity.
I have attempted to apply adaptive threshold, but the performance is not good for the following characteristic:
Mean: The value u depends on high frequency component of the sequence
Image variation: The HMM detection is pixel-wise. The pixel sequence variation has weak relationship with image variation
Pixel variation: Overlap with HMM
If we want to systematically process numerous frames. We can apply a general threshold e.g. 0.2 for a scene. This will cause false alarm.
In some cases, false alarms also occur at very strong unsteadiness or motion region.
Limitation of Thresholding
Cancel unsteadiness

## Slide 18
03 HMM Detection and Restoration
Given two neighboring frames, Pyramidal Lucas-Kanade motion tracker can estimate the motion magnitude and orientation of each pixel.
3. Apply the Lucas-Kanade motion tracker and eliminate the strong motion region to obtain purer detection result.
For example, in this frame a man is walking inside the store. The motion intensity is represented by brightness and the orientation is represented by Hue.
Cancel motion

## Slide 19
03 HMM Detection and Restoration
4. Use inpainting to restore the image
Artifact is removed and replaced by neighboring pixels
Apply to
Inpainting procedure starts from the boundary and compute the perpendicular orientation. Then it repeatedly replace the inner oriented neighbor with the outer neighbor until the hole is fully filled.

## Slide 20
03 HMM Detection and Restoration
For bulk restoration, the accuracy is inevitably lower.
Accurate detection
False Alarm
Using general threshold of 0.2

## Slide 21
03 HMM Detection and Restoration
Limitation of HMM
Pixel-wise Examination – High demands on both GPU and CPU
Need the previous 6 frames and the following 6 frames to assist detection
The detection performance is good by applying manual thresholding. If we apply a general threshold, false alarms need to be eliminated.
Set up:
Anaconda
Jupyter notebook
CPU: Intel I7 7th Gen
GPU: GTX1060
Python
PyTorch
All arrays are computed as tensors in GPU
Score (u value) map generation:
6000 seconds / 1300*2100pixels
0.002197 seconds /pixel
~500 pixels / second
False alarm elimination
5 seconds/frame
Restoration:
5-60 5 seconds/frame
Depending on the number of artifacts

## Slide 22
03 HMM Detection and Restoration
Program Preview

## Slide 23
CNN Detection and Restoration
PART 04

## Slide 24
04 CNN Detection and Restoration
Artifacts detection in CNN is a binary semantic segmentation task.
(Normal Region = Class 0, Artifact region = Class 1)
The popular model “SegNet”is selected as the referencing model.
Main idea of CNN Detection
The artifact feature is much simpler than typical objects of semantic segmentation (tree, cars, houses).
The network complexity can be further reduced as proposed in [6].
[6] H. Yous, A. Serir, and S. Yous,“Cnn-based method for blotches and scratches detection in archived videos,” Journal of Visual Communication and Image Representation, vol.59, pp. 486–500,2019, ISSN: 1047-3203
Remove Batchnorm Layers
Reduce number of Convolution, ReLU and Pooling layers

## Slide 25
04 CNN Detection and Restoration
Main idea of CNN Detection
Remove Batchnorm Layers
Reduce number of Convolution, ReLU and Pooling layers
Batchnorm layer is to prevent the training from falling into dead band. Using an initializer can be a substitute.
If the simplified model can achieve satisfactory performance as well, reducing the layers can further increase the computation speed and reduced the dataset size.
Simplify

## Slide 26
04 CNN Detection and Restoration
Original Image Set
Ground Truth
Training preparation:
Compare the original and ground truth. Pixel with intensity difference larger than 50 is labeled as artifact
Segment one frame to 24 256*256 frames.
Discard a frame if artifact number <10.
Compare and Segment
Input
Label
In order to train the CNN network, we prefer a dataset that provides:
Images that have artifacts with regular boundaries.
Pixelwise artifact labeling instead of region labeling
However, we have not found a good quality dataset from online resources yet and hence, we decide to build our own dataset.
Customized Dataset

## Slide 27
04 CNN Detection and Restoration
(continue)Training preparation:
Compare the original and ground truth. Pixel with intensity difference larger than 50 is labeled as artifact.
Segment one frame to 24 256*256 frames.
Discard a frame if artifact number <10.
Customized Dataset Limitation
The reason why the classifying threshold is 50 but not zero is
Some irregular regions are brightened or darkened after restoration, which is hard to solve using regional histogram equalization.
Our target artifacts are white blotches but there are other artifacts such as green flickers that may mislead the training.
White blotches are high-intensity artifacts. Unless the background is bright as well, the blotches can be easily detected.
We also observed that
1. GPU memory required by large frames exceeds my setup.
2. The normal-to-artifact ratio is too high. We segment the frame into small subframes and discard all useless frames.

## Slide 28
04 CNN Detection and Restoration
Initializer: Xavier
Loss Function: Weighted Binary Cross-Entropy Loss
Optimizer: SGD
Learning Rate: 0.1
Momentum: 0.9
Class Balancing
The defect frequency is 0.0118 and the normal frequency is 0.9882, the median of the two classes is 0.5 ((0+1)/2=0.5). The weighted assigned to each class is the median of class divided by the frequency of each class
=42.3729
=0.5059
Selected Training Utilities
With the help of Xavier, we can initialize the weights of the network so that the neuron activation functions will not start from saturated regions.
Less likely to be trapped in local minimum
We train the network using 7918 images, batch size = 4 and run 10 epochs.

## Slide 29
04 CNN Detection and Restoration
1. Perform thresholding to obtain initial defect map of the current frame and the next frame.
Artifact is covered
2. Eliminate the candidates appearing in neighboring frames
3. Use inpainting method for restoration
Artifacts are replaced by neighboring pixels
The network output a 256*256 values that ranges from 0-1

## Slide 30
04 CNN Detection and Restoration
Accurate detection
False alarm
Accurate detection
Missing detection
Much better than HMM

## Slide 31
Deep Image Prior Denoising
PART 05

## Slide 32
05 Deep Image Prior Denoising
The result demonstrates the feature order a DNN learns. The best results (2400 iterations) appear in the middle of the training.
Main idea of Deep Image Prior
Deep Image Prior utilize the characteristic of deep convolution network that learns and copies the "natural" features prior to "corrupted" ones.
The generator network inside first learn and encode the low frequency, regular, natural features.
Interrupt here

## Slide 33
05 Deep Image Prior Denoising
Training Details:
https://github.com/DmitryUlyanov/deep-image-prior
Learning rate=0.01
Input_depth = 3
Nonlinearity function: Sigmoid
Activation function: LeakyReLU

## Slide 34
05 Deep Image Prior Denoising
Training results after 1200, 2400, 3600, 4800, 6000, and 7200 iterations
White spot appears
White spot appears

## Slide 35
05 Deep Image Prior Denoising
Results after 7200 iterations
Original image
Observation:
It may not be able to remove the artifacts, but it can soften or denoise them.

## Slide 36
05 Deep Image Prior Denoising
Limitation
Deep image prior is only a global denoising technique, which generates no defect map. Hard to measure the restoration performance.
Hard to find the best interrupt point, where the resolution is high enough and artifacts less enough.

## Slide 37
Conclusion
PART 06

## Slide 38
06 Conclusion
Conclusion
HMM detection and restoration
Require thresholding for each frames to secure good performance. If setting a general threshold, false alarm elimination is needed.
HMM detection is pixel-wise that leads to high computational effort.
Need neighboring frames for sequence examination
CNN detection and restoration
The detection accuracy is much higher than HMM method. False alarms are also fewer.
Most of the computation can be accelerated by GPU and hence much faster than HMM method.
Can perform using a single frame
Deep Image Prior
Can only denoise the artifacts and conceal some small spikes.
The performance can only be measured intuitively.

## Slide 39
06 Conclusion
Reference
[2] Kokaram, A. C., & Rayner, P. J. System for the removal of impulsive noise in image sequences. In Visual Communications and Image Processing'92 (Vol. 1818, pp. 322-331). International Society for Optics and Photonics, 1992.
[1] R. Storey,“Electronic detection andconcealment of film dirt,” J. Soc. Motion Picture Telev.
Eng., vol.94, no.6, pp.642–647, Jun.1985.
[3] X. Wang and M. Mirmehdi, "Archive Film Defect Detection and Removal: An Automatic Restoration Framework," in IEEE Transactions on Image Processing, vol. 21, no. 8, pp. 3757-3769, Aug. 2012.
[5] A. Krizhevsky, I.Sutskever, and G.E.Hinton,“Imagenet classification with deep convolutional neural networks,” Communications of the ACM, vol.60, no.6, pp.84–90, 2017.
[4] Y. LeCun, L. Bottou, Y. Bengio, and P. Haffner,“Gradient-based learning applied to document recognition,” Proceedings of the IEEE, vol.86, no.11, pp.2278–2324,1998.
[6] H. Yous, A. Serir, and S. Yous,“Cnn-based method for blotches and scratches detection in archived videos,” Journal of Visual Communication and Image Representation, vol.59, pp. 486–500, 2019, ISSN: 1047-3203

## Slide 40
Thank you for your watching!